## Slide 1: Pin OUT Arduino DIP
Vin
Low side PWM, 6A, 30V
Channel T0,T1,T2,T3
GND
Vout
GND
4x Transistor
on Bottom or Motor driver + Inverter on the top layer!
PC1
Direct connected to CHIP GPIO 7
PD2
PB3
UART header
ICSP header
Accel header connected to
CHIP I2C_2
PC3
PC2
PD3
PB0
Atmega pin | DIP pin | Arduino Pin | Digital IN/OUT | Analog IN | PWM out | WS2812 support
PB0 | 11 | 8 | X |  |  | X
PD3 | 9 | 3 | X |  | X | X
PC3 | 10 | 17 | X | X |  | 
PB3 | 7 | 11 | X |  | X | X
PD2 | 6 | 2 | X |  |  | X
PC1 | 4 | 15 | X | X |  | 
PC2 | 8 | 16 | X | X |  | 
PB2 | 0 | 10 | */X |  | X | *
PB1 | 1 | 9 | */X |  | X | *
PD6 | 2 | 6 | */X |  | X | *
PD5 | 3 | 5 | */X |  | X | *
* Only without transistor
And a little solder bridge

## Slide 2: Jumper Config Arduino DIP
Vin
Low side PWM, 6A, 30V
Channel T0,T1,T2,T3
GND
Vout
GND
PC1
Direct connected to CHIP GPIO 7
PD2
PB3
SJ1
SJ2
SJ3
SJ4
SJ5
SJ | Function
1 | Vin to Charge in If your input voltage is 5V close this jumper. Your Vin will charge your Battery
2 | Vout to Vcc If your Vin is not 5V close it, to get CHIP 5V on the output If your Vin is 5V and you close SJ5, close this one to power the DIP from the VIN, in this case you must leave SJ3 and SJ4 open!
3 | CHIP 5V to Vcc If you won’t power the DIP via VIN, close this jumper to supply 5V power via the CHIP If you destroyed your CHIP onboard 5V, close it to supply power to the USB
4 | CHIP 3.3V to Vcc If you want to work the DIP on the (limited) 3.3V of the CHIP
5 | Vin to Vout To forward your input to the output
Never combine: SJ3 and SJ4 and
SJ4, SJ2, SJ5 and supply power via Vin/Vout and
SJ3, SJ2, SJ5 and supply power via Vin/Vout and
SJ1 if your Vin is NOT ~5V and SJ2, SJ5 if your Vin > 5V
Combine: SJ1, SJ5, SJ2 if your Vin is 5V or
SJ2, SJ3 if you only draw a few mA