## Slide 1
JKW boards – Confusion avoidance chart  LEDv1.1 / Motor v1.1 / preSalsa / Salsa / Salsa II / Queso DIP
Function X = possible - = not possible * = ‘Or’ .. E.g. Motor OR Mosfet / Optional | Motor v1.1 | LEDv1.1 | PreSalsa | Salsa | Salsa II | Queso
Screw terminals that connects an external power supply to CHIP CHR-IN | X | X | X | X | X | X
Controller connected via I2C | - | X | X | X | X | -
Pins for driving ws2812 LEDs | - | X | X | X | X | -
Pins for analog reading | - | X | X | X | X | -
“Real-time” GPIOs | - | X | X | X | X | -
Mosfets to dim a lot of LEDs | - | 4 | 4* | 4* | 4*/2X | -
Motor driver Channels | 2 | - | 2* | 2* | 2*/1X | -
Input for “High voltage” (~7V for the Motor) | X | - | - | - | X | -
Internal connection to CHIP power button pin, e.g. to start the CHIP from power off, or to shut the CHIP down | - | - | - | X | X | -
“Seamless power” (run on CHIP battery, with CHIP powered down) | - | - | - | - | X | -
Option for onboard power supply (DC in 7-28V) | - | - | - | - | X | X
CHIP pins used by board (besides I2C bus which is not exclusively used) | *4 | *1 | *5 | *6 | *6 | -
On board Ws2812 LED option | - | - | - | * | * | -
On board general purpose button (e.g. shutdown for CHIP?) | - | - | - | - | * | -
On board general purpose LED | - | - | X | * | * | -
4x USB Hub | - | - | - | - | - | X
preSalsa, Salsa and Salsa II can all be assembled as Dual-channel (4 outputs) Motor driver OR 4-channel Mosfet - PWM Driver
(Salsa II can be configured as 1 channel motor AND 2 channel Mosfet – PWM)

## Slide 2
Salsa II DIP Photos
ORDERED 2016/03/03
Configuration PWM dimmer
Configuration Motor driver

## Slide 3
Vin
Low side PWM, 6A, 30V
Or Motor Driver, 600mA
Channel P0,P1,P2,P3
GND
Vout
GND
4x Transistor
+ Inverter on Bottom and Motor driver + power supply on the top layer!
P4
Direct connected to CHIP GPIO 7
P6
P7
UART header
GND
-
-
PC TX
PC RX
Reset
ICSP header
Accel header connected to
CHIP I2C_2
P10
P8
P9
P12
* Only without transistor
and a little solder bridge
P11
GLED or
Ws2812 or button
Atmega pin | DIP pin | Arduino Pin | Digital IN/OUT | Analog IN | PWM out | WS2812 support | C.H.I.P. pin | Motor Pins
PC0 | P16 | 14 | X | - | - | - | - | -
PD4 | P15 | 4 | X | - | - | - | - | -
PB5 | P14 | 13 | X | - | - | - | - | DL
PB4 | P13 | 12 | X | - | - | - | - | DR
PD7 | P12 | 7 | X | - | - | X | - | -
PB0 | P11 | 8 | X | - | - | X | - | -
PC3 | P10 | 17 | X | X | - | - | - | -
PD3 | P9 | 3 | X | - | X | X | - | ER
PC2 | P8 | 16 | X | X | - | - | - | -
PB3 | P7 | 11 | X | - | X | X + On board | - | -
PD2 | P6 | 2 | X | - | - | X | - | -
- | P5 | - | - | - | - | - | X | -
PC1 | P4 | 15 | X | X | - | - | - | -
PD5 | P3 | 5 | */X | - | X | * | - | -
PD6 | P2 | 6 | */X | - | X | * | - | -
PB1 | P1 | 9 | */X | - | X | * | - | -
PB2 | P0 | 10 | */X | - | X | * | - | EL
Salsa II DIP PinOut

## Slide 4
Queso DIP v4.3 Photos
ORDERED 2016/03/01
EXPECTED 2nd Week of April
Test-board-photos

## Slide 5
Queso DIP v4.3 PinOut
ORDERED 2016/03/01
4x USB-A to the bottom of the board
Can carry one (recommended) or up to two DCDC regulator
Power IN via
Screw-Terminals
7-28V DC in, 5V
3A out
Port activity LEDs
Micro USB
Input jack

## Slide 6
ONION DIP v1.0 Photos
ORDERED 2016/03/16
NOT YET RECEIVED

## Slide 7
ONION DIP v1.0 PINOUT1/2
ORDERED 2016/03/16
NOT YET RECEIVED
Stand-alone tinker area for DIL ICs with power rails left & right
Optional: Relay to switch e.g. 110/230V AC Power lines @ 10A
Screw terminal for Relay contacts:
N_close, In, N_out
Standard USB-UART Connector
2x I2C-2
2x SPI-2
GPIO P0-P5, each pin twice
3x LED, P0 &P3 active low,
On Relay closed
Optional: DC-DC regulator to power the CHIP from 7-28V DC, covering tinker area
Optional: MOSFET on P0 (active high) to drive the relay
Screw terminal for power in
Battery pins

## Slide 8
ONION DIP v1.0 PINOUT2/2
ORDERED 2016/03/16
NOT YET RECEIVED
GND Rails highlighted
CHIP 3.3V Rails
5V Rails highlighted

## Slide 9: Old boards
The following pages show old boards, which are not longer produced:
LED DIP v1.1
preSalsa DIP
Salsa I
Motor Dip v1.1

## Slide 10
LED DIP v1.1 Photo

## Slide 11: LED DIP v1.1 PinOut
Vin
GND
Vout
GND
4x Transistor
on Bottom or Motor driver + Inverter on the top layer!
P4
Direct connected to CHIP GPIO 7
P6
P7
UART header
GND
-
-
PC TX
PC RX
Reset
ICSP header
P10
P8
P9
P12
Atmega pin | DIP pin | Arduino Pin | Digital IN/OUT | Analog IN | PWM out | WS2812 support | C.H.I.P. connection
PD7 | P12 | 7 | X | - | - | X | -
PB0 | P11 | 8 | X | - | - | X | -
PC3 | P10 | 17 | X | X | - | - | -
PD3 | P9 | 3 | X | - | X | X | -
PC2 | P8 | 16 | X | X | - | - | -
PB3 | P7 | 11 | X | - | X | X | -
PD2 | P6 | 2 | X | - | - | X | -
- | P5 | - | - | - | - | - | X
PC1 | P4 | 15 | X | X | - | - | -
PD5 | P3 | 5 | */X | - | X | * | -
PD6 | P2 | 6 | */X | - | X | * | -
PB1 | P1 | 9 | */X | - | X | * | -
PB2 | P0 | 10 | */X | - | X | * | -
* Only without transistor
And a little solder bridge
P11
Low side PWM, 6A, 30V
Or Motor Driver, 600mA
Channel P0,P1,P2,P3

## Slide 12
preSalsa DIP Photo
Motor Version ->
LED Driver / Mosfet Version

## Slide 13: preSalsa DIP PinOut
Vin
Low side PWM, 6A, 30V
Or Motor Driver, 600mA
Channel P0,P1,P2,P3
GND
Vout
GND
4x Transistor
on Bottom or Motor driver + Inverter on the top layer!
P4
Direct connected to CHIP GPIO 7
P6
P7
UART header
GND
-
-
PC TX
PC RX
Reset
ICSP header
Accel header connected to
CHIP I2C_2
P10
P8
P9
P12
Atmega pin | DIP pin | Arduino Pin | Digital IN/OUT | Analog IN | PWM out | WS2812 support | C.H.I.P. connection
PD7 | P12 | 7 | X | - | - | X | -
PB0 | P11 | 8 | X | - | - | X | -
PC3 | P10 | 17 | X | X | - | - | -
PD3 | P9 | 3 | X | - | X | X | -
PC2 | P8 | 16 | X | X | - | - | -
PB3 | P7 | 11 | X | - | X | X | -
PD2 | P6 | 2 | X | - | - | X | -
- | P5 | - | - | - | - | - | X
PC1 | P4 | 15 | X | X | - | - | -
PD5 | P3 | 5 | */X | - | X | * | -
PD6 | P2 | 6 | */X | - | X | * | -
PB1 | P1 | 9 | */X | - | X | * | -
PB2 | P0 | 10 | */X | - | X | * | -
* Only without transistor
And a little solder bridge
P11

## Slide 14: PreSalsa Jumper Config
Vin
Low side PWM, 6A, 30V
Channel T0,T1,T2,T3
GND
Vout
GND
PC1
Direct connected to CHIP GPIO 7
PD2
PB3
SJ1
SJ2
SJ3
SJ4
SJ5
SJ | Function
1 | Vin to Charge in If your input voltage is 5V close this jumper. Your Vin will charge your Battery
2 | Vout to Vcc If your Vin is not 5V close it, to get CHIPs 5V on the output If your Vin is 5V and you close SJ5, close this one to power the DIP from the VIN, in this case you must leave SJ3 and SJ4 open!
3 | CHIP 5V to Vcc (bot) If you won’t power the DIP via VIN, close this jumper to supply 5V power via the CHIP If you’ve destroyed your CHIP onboard 5V, close it to supply power to the USB 
4 | CHIP 3.3V to Vcc (bot) If you want to work the DIP on the (limited) 3.3V of the CHIP
5 | Vin to Vout To forward your input to the output
Never combine: SJ3 and SJ4 or
SJ4 + SJ2 + SJ5 and supply power via Vin/Vout or
SJ3 + SJ2 + SJ5 and supply power via Vin/Vout or
SJ1 if your Vin is NOT ~5V or SJ2 + SJ5 if your Vin > 5V
Combine: SJ1 + SJ5 + SJ2 if your Vin is 5V or
SJ2 + SJ3 if you only draw a few mA to use the CHIPs 5V

## Slide 15
Salsa DIP Photos
WAITING ON CHINA POST
ORDERED 2016/02/10
Configuration PWM dimmer
Configuration Motor driver

## Slide 16: Salsa DIP PinOut
Vin
Low side PWM, 6A, 30V
Or Motor Driver, 600mA
Channel P0,P1,P2,P3
GND
Vout
GND
4x Transistor
on Bottom or Motor driver + Inverter on the top layer!
P4
Direct connected to CHIP GPIO 7
P6
P7
UART header
GND
-
-
PC TX
PC RX
Reset
ICSP header
Accel header connected to
CHIP I2C_2
P10
P8
P9
P12
* Only without transistor
And a little solder bridge
P11
Micro USB
Ws2812 or LED
Atmega pin | DIP pin | Arduino Pin | Digital IN/OUT | Analog IN | PWM out | WS2812 support | C.H.I.P. pin | Motor Pins
PC0 | P16 | 14 | X | - | - | - | - | -
PD4 | P15 | 4 | X | - | - | - | - | -
PB5 | P14 | 13 | X | - | - | - | - | DL
PB4 | P13 | 12 | X | - | - | - | - | DR
PD7 | P12 | 7 | X | - | - | X | - | -
PB0 | P11 | 8 | X | - | - | X | - | -
PC3 | P10 | 17 | X | X | - | - | - | -
PD3 | P9 | 3 | X | - | X | X | - | ER
PC2 | P8 | 16 | X | X | - | - | - | -
PB3 | P7 | 11 | X | - | X | X | - | -
PD2 | P6 | 2 | X | - | - | X | - | -
- | P5 | - | - | - | - | - | X | -
PC1 | P4 | 15 | X | X | - | - | - | -
PD5 | P3 | 5 | */X | - | X | * | - | X
PD6 | P2 | 6 | */X | - | X | * | - | -
PB1 | P1 | 9 | */X | - | X | * | - | -
PB2 | P0 | 10 | */X | - | X | * | - | EL

## Slide 17
Motor DIP v1.1 Photos

## Slide 18: Motor DIP v1.1 Pin Out
Vin
GND
VHin
GND
Motor
Driver IC
L293DD
P4
P5
P6
P7
Status LED
Inverter
P9
P0
P1
P2
P3
Accel
Header for
Sparkfun:
MMA8452Q Connected to CHIP I2C bus
# | Function
Vin | Logic voltage, 5V
P0 | Channel 1 direction
P1 | Channel 1 enable
P2 | Channel 3 direction
P3 | Channel 3 enable
GND | Ground for logic voltage
VHin | “High” voltage for Motor (5-36 Volt), can be connected to Vin
P4 | Channel 1 output
P5 | Channel 2 output (inverse of channel 1)
P6 | Channel 3 output
P7 | Channel 4 output (inverse of channel 3)
GND | Ground for “high” voltage
CHIP GPIO P0, P1, P2, P3 can be used instead of screw header

## Slide 19
Vin
GND
VHin
GND
Motor
Driver IC
L293DD
P4
P5
P6
P7
Status LED
(resistors on bot,
LED and resistor aren’t populated)
SJ1-4
P9
P0
P1
P2
P3
Accel
Header for
Sparkfun:
MMA8452Q Connected to CHIP I2C bus
SJ | Function
1-4 | Use CHIP GPIO as input Close them, if you use the CHIP GPIO to generate the control signals. Leave them open if you want to use the screw header
5 | Vin to Charge in Close it if you Vin is 5V from a power supply or external battery to power this CHIP over this pin as well Leave it open, if you feed the CHIP 5V to the Vin
CHIP GPIO P0, P1, P2, P3 can be used instead of screw header
SJ5
Motor DIP v1.1 Jumper Config

## Slide 20: More photos