## Slide 1: Pin OUT v1.1 Motor DIP
Vin
GND
VHin
GND
Motor
Driver IC
L293DD
P4
P5
P6
P7
Status LED
Inverter
P9
P0
P1
P2
P3
Accel
Header for
Sparkfun:
MMA8452Q Connected to CHIP I2C bus
# | Function
Vin | Logic voltage, 5V
P0 | Channel 1 direction
P1 | Channel 1 enable
P2 | Channel 3 direction
P3 | Channel 3 enable
GND | Ground for logic voltage
VHin | “High” voltage for Motor (5-36 Volt), can be connected to Vin
P4 | Channel 1 output
P5 | Channel 2 output (inverse of channel 1)
P6 | Channel 3 output
P7 | Channel 4 output (inverse of channel 3)
GND | Ground for “high” voltage
CHIP GPIO P0, P1, P2, P3 can be used instead of screw header